## Slide 1: Linux Network Programming with P4
Linux Plumbers 2018
Fabian Ruffy, William Tu, Mihai Budiu
VMware Inc. and University of British Columbia

## Slide 2: Outline
Introduction to P4
XDP and the P4 Compiler
Testing
Example
Performance Results
Discussion
Fabian
William

## Slide 3: What is P4?
High-level programming language for network data planes
  Allows for protocol flexibility
  Specifies a packet processing pipeline
Compiled and loaded into target platform
Open and standardized
P4: Programming Protocol-Independent Packet Processors
Pat Bosshart, Dan Daly, Glen Gibb, Martin Izzard, Nick McKeown, Jennifer Rexford, Cole Schlesinger, Dan Talayco, Amin Vahdat, George Varghese, David Walker ACM SIGCOMM Computer Communications Review (CCR). Volume 44, Issue #3 (July 2014)

## Slide 4: P4 Essentials
C-like, strongly typed language
Type and memory-safe (no pointers)
Bounded execution (no loops)
Statically allocated (no malloc, no recursion)
Spec: http://github.com/p4lang/p4-spec
Reference compiler implementation: http://github.com/p4lang/p4c (Apache 2 license)

## Slide 5: P4 Software Workflow
P4 Architecture
Model
P4 Compiler
Target-specific configuration binary
Data Plane
Tables
Extern
objects
Load
Target
Supplied
P4 Program
User-supplied
Control Plane
Add/remove table entries
CPU port
Packet-in/out
Extern control
RUNTIME

## Slide 6: P416 generic data-plane model
os_lib.p4
switch_lib.p4
npu_lib.p4
nic_lib.p4
program.p4
The networking stack of the OS

## Slide 7: P4 and XDP

## Slide 8: eBPF/XDP
Virtual machine running in the Linux kernel
Provides:
  The ability to write restricted C and run it in the kernel
  A set of kernel hook points invoking the eBPF program
  Extensible, safe and fast
  Alternative to user-space networking
Example of TC+eBPF
driver
Hardware
tc
Bridge hook
IP/routing
socket
Kernel
space
User space
eBPF hook point
Your Program
A programmable data plane in the Linux kernel!

## Slide 9: P4 vs eBPF/XDP
Feature | P4 | eBPF/XDP
Level | High | Low
Safe | Yes | Yes
Safety | Type system | Verifier
Loops | In parsers | Tail calls (dynamic limit)
Resources | Statically allocated | Statically allocated
Policies | Tables (match+action) | Maps (tables)
Extern helpers | Target-specific | Hook-specific
Control-plane API | Synthesized by compiler | eBPF maps

## Slide 10: The P4 eBPF backends
p4c-xdp
p4c-ebpf is part of the open-source distribution
  http://github.com/p4lang/p4c/backends/ebpf
p4c-xdp is a separate open-source project
  http://github.com/vmware/p4c-xdp
  Extension of the p4c compiler
  Reuses much of the code
Not production-ready
  Needs more work
  Known bugs and limitations
  Generated not efficient yet
p4c-ebpf

## Slide 11: Generating XDP code

## Slide 12: P416 -> C -> eBPF/XDP
Generates stylized C
No tail calls yet, all data on stack
eBPF tables control/data-plane communication
Can do filtering, forwarding, encapsulation
Relies on Linux TC for forwarding
  We plan on switching to libbpf

## Slide 13: The XDP Switching Model
Parser
Match+
Action
Deparser
XDP Data Plane
packet in
packet out
EBPF tables
Control-plane API
Drop/Forward/Pass
Input port
headers
headers

## Slide 14: Flow
app.p4
Clang + LLVM
Data Plane XDP driver
Verifier
app.h
BPF system call
Hardware
Kernel space
User space
app.c
p4c-xdp
control-plane.c
Control-plane API
app.o
exe
Match-Action
tables

## Slide 15: Testing P4-XDP code

## Slide 16: Test Frameworks
User-space testing
  Isolates specification from implementation
  Validates correctness of generated code
  User-space wrappers around eBPF tables and APIs
  Reads and writes packets from capture files
Kernel-space testing
  Loads eBPF program into kernel
  I/O connected to virtual interfaces
  Writes capture files to interfaces in user-space
  Records output using tcpdump

## Slide 17: Five Testing Stages
compile p4
compile data-plane
check results
test.stf
expect0.pcap
expect1.pcap
….
input0.pcap
input1.pcap
….
output0.pcap
output1.pcap
….
pass/
fail
parse stf
run
test.p4
runtime executable
runtime source
1
5
3
2
4

## Slide 18: A sample P4-XDP program

## Slide 19: Forwarding an IPv4 Packet
Parse Ethernet and IPv4 header
Lookup a table using Ethernet’s destination as key
Based on Ethernet’s destination address, execute one action:
  Drop the packet (XDP_DROP)
  Pass the packet to network stack (XDP_PASS)
Parser
Match+
Action
Deparser
Drop
Network stack
packet

## Slide 20: P4 Headers
struct Ethernet{ u8 source[6]; u8 destination[6]; u16 protocol; u8 ebpf_valid; }
struct IPv4 { u8 version[6]; /* bit<4> */ u8 ihl[6]; /* bit<4> */ u8 diffserv; /* bit<8> */
header Ethernet { bit<48> source; bit<48> dest; bit<16> protocol; }
header IPv4{ bit<4> version; bit<4> ihl; bit<8> diffserv; … }
struct Headers { Ethernet eth; IPv4 ipv4; }
C struct + valid bit
p4c-xdp
Currently each header field is re-aligned
Inefficient design
Notes: struct IPv4 { u8 version; /* bit<4> */ u8 ihl; /* bit<4> */ u8 diffserv; /* bit<8> */ u16 totalLen; /* bit<16> */ u16 identification; /* bit<16> */ u8 flags; /* bit<3> */ u16 fragOffset; /* bit<13> */ u8 ttl; /* bit<8> */ u8 protocol; /* bit<8> */ u16 hdrChecksum; /* bit<16> */ u32 srcAddr; /* bit<32> */ u32 dstAddr; /* bit<32> */ u8 ebpf_valid;};

## Slide 21: P4 Protocol Parser
﻿parser Parser(packet_in packet, out Headers hd) {
state start { packet.extract(hd.ethernet); transition select(hd.ethernet.protocol) { 16w0x800: parse_ipv4; default: accept; }
state parse_ipv4 { packet.extract(hd.ipv4); transition accept; }}
struct Headers hd = {};
…
if (end < start + header_size)
goto reject;
hd.ethernet.destination[0] = load_byte(…);
…
p4c-xdp

## Slide 22: Match-Action
﻿control Ingress (inout Headers hdr,
in xdp_input xin, out xdp_output xout) {
action Drop_action() { xout.output_action = xdp_action.XDP_DROP; }
action Fallback_action() { xout.output_action = xdp_action.XDP_PASS; }
table mactable {
key = {hdr.ethernet.destination : exact; }
actions = { Fallback_action; Drop_action; }
implementation = hash_table(64); } … }
﻿struct mactable_key {
u8 field0[6];
}
enum mactable_actions {
Fallback_action,
Drop_action,
}
struct mactable_value {
enum mactable_actions action;
union {
struct {
} Fallback_action;
struct {
} Drop_action;
} u;
}
p4c-xdp

## Slide 23: Control-plane API in C
﻿#include ”xdp1.h”
int main () {
int fd = bpf_obj_get(MAP_PATH);
…
struct mactable_key key;
memcpy(key.field0, MACADDR, 6);
struct mactable_value value;
value.action = Fallback_action;
bpf_update_elem(fd, &key, &value, BPF_ANY);
}
Generated by compiler

## Slide 24: Deparser: Update the Packet
﻿control Deparser(in Headers hdrs, packet_out packet) { apply { packet.emit(hdrs.ethernet); packet.emit(hdrs.ipv4); }}
bpf_xdp_adjust_head(skb, offset); ebpf_byte = ((char*)(&hd.ethernet.destination))[0];
write_byte(ebpf_packetStart, BYTES(ebpf_packetOffsetInBits) + 0, ebpf_byte);
…
ebpf_packetOffsetInBits += 48;
p4c-xdp

## Slide 25: Complete C program structure
﻿SEC(“prog”) int ebpf_filter(struct xdp_md *skb) { struct Headers hd = {}; …
/* parser */ if (end < start + header_size) goto reject;
hd.ethernet.destination[0] = load_byte(…); …
/* match+action*/ value = bpf_map_lookup_elem(key); switch(value->action) { case Drop_action: … }
/* deparser */ xdp_adjust_head(amount);
// update packet header
return xout.xdp_output; }
Parser:
  Check packet access boundary.
  Walk through the protocol graph.
  Save in “struct Headers hd.”
Match+Action:
  Extract key from struct Headers
  Lookup BPF hash map
  Execute the correponding action
Deparser
  Convert headers back into a byte stream.
  Only valid headers are emitted.

## Slide 26: Performance Benchmarks

## Slide 27: Performance Evaluation
P4C-XDP binary
  #./p4c-xdp --target xdp -o <output_file> <input p4>
  Sample code at tests/xdp*.p4
  Load to driver by: ip link set dev eth0 xdp obj xdp1.o
Measure packet rate in Mpps
  Packet drop rate (XDP_DROP) and transmit rate (XDP_TX)
16-core Intel Xeon
E5 2650 2.4GHz
32GB memory
Intel X540 10GbE
Ixgbe driver
sender
Intel X540 10GbE
ixgbe driver with XDP
Linux kernel
4.19-rc5
P4C-XDP
UDP 14Mpps

## Slide 28: Sample P4 Program Performance
SimpleDrop: return XDP_DROP
xdp1.p4: parse Ethernet/IPv4 header, deparse it, and drop.
xdp3.p4: parse Ethernet/IPv4 header, lookup a MAC address in a map, deparse it, and drop.
xdp6.p4: parse Ethernet/IPv4 header, lookup and get a new TTL value from eBPF map, set to IPv4 header, deparse it, and drop.
Possible Optimization: avoid byte-order translation and unnecessary (de-)parsing
P4 Program | Performance (Mpps) | Possible Optimization
SimpleDrop | 14.4 | NA
xdp1 | 8.1 | 14
xdp3 | 7.1 | 13
xdp6 | 2.5 | 12

## Slide 29: Limitations

## Slide 30: Fundamental Limitations
Feature | P4 | XDP
Loops | Parsers | Tail call
Nested headers | Bounded depth | Bounded depth
Multicast/broadcast | External | No
Packet segmentation | No | No
Packet reassembly | No | No
Timers/timeouts/aging | No | No
Queues | No | No
Scheduling | No | No
State | Registers/counters | Maps
Linear scans | No | No

## Slide 31: Limitations of XDP
No multi-/broadcast support
  No ability to clone packets in XDP
The stack size is too small
  Complex pipelines are rejected by the verifier
Generic XDP and TCP
  TCP is ignored by the generic XDP driver
eBPF maps cannot be pinned in network namespaces

## Slide 32: Conclusion
P4 is a language that defines data-path behavior
  It generalizes to different architectures
  Including the Linux kernel
P4 can express XDP
  High-level abstraction to C code
  Generated code is performant but not optimal
  Many future optimizations are possible
P4 and XDP have similar limitations