## Slide 1: Incremental Specialization of Network Programs
Fabian Ruffy, Zhanghan Wang (New York University),
Gianni Antichi (Politecnico di Milano),
Aurojit Panda, Anirudh Sivaraman (New York University)

## Slide 2: Specializing Network Devices
Control-plane API
Programmable network device
Packets
Optimizing compiler
Control plane
Program
Forward
Parse Ethernet
Parse IPv4
Parse IPv6
Tunnel
Drop

## Slide 3: Specializing Network Devices
Control-plane API
Programmable network device
Packets
Control plane
Program
Forward
Parse Ethernet
Parse IPv4
Parse IPv6
Tunnel
Drop
Specialization inputs
Specializing compiler
Control plane rules
Traffic workload
Optimizing compiler
CPUs: fewer branches and instructions!
Switch ASICs: space for other NFs!
FPGAs: a little bit of both!
ESwitch (SIGCOMM’16)
HODA (EuroSys’24)
Morpheus (ASPLOS’22)
Pipeleon (SIGCOMM’23)

## Slide 4: Your Optimization Inputs Can And Will Change
Control-plane API
Programmable network device
Packets
Control plane
Program
Forward
Parse Ethernet
Parse IPv6
Drop
Specialization inputs
?
Insert drop rules!
Specializing compiler
Your program is stale!
  Degree of Staleness
Respecialize on
every update
Respecialize in
fixed intervals
Resolving program staleness
Incremental respecialization (only when necessary)

## Slide 5: Three Observations We Can Use To Our Advantage
Traffic workloads are measured. Control-plane configurations are defined.
Many control-plane updates are only targeting a specific program element.
Many control-plane updates don’t affect semantics in your source program.

## Slide 6: Incremental Specialization
  Network device program
ACL
ACL
Specialization shim
Control plane
Parser
Tunnel
Update: “Remove all drop rules”
Affected?
Behavior change?
Recompile
ACL*
Compiler
Specialization inputs

## Slide 7: Does Incremental Specialization Work?
We implemented partial evaluation for P4.
Dead code removal, constant substitution, table inlining.
Control-plane specialization can already save resources.
Our analysis saved 20% stages on a SCION Tofino program.
The specialization is incremental.
We process profile updates and make a decision within 100ms.
There are challenges and limitations course!
Please see our paper for implementation details.

## Slide 8: Where We Are Stuck: The Ecosystem Is Not There Yet
Specialization shim
Control plane
  Network device program
A
A
Recompile
ACL*
Compiler
Specialization inputs
Parser
Tunnel
Enablers for incremental specialization
Incremental compilation: only recompile the pieces that changed.
Partial reconfiguration: change program modules disruption-free.

## Slide 9: Projects For The Community
Realizing partial reconfiguration and incremental recompilation.
Explore trade-offs between specialization quality and specialization durability.
Apply incremental specialization to the rest of the network.
Consider reintegrating traffic information as optimization input. Reliably!
Project Repository: https://github.com/nyu-systems/flay

## Slide 10: Specialized Networks
I only have IPv6/UDP traffic and I only configure GRE, not VXLAN!
IPv4
TCP
VXLAN
UDP
IPv6
Control plane
Programmable data plane
Specializer
GRE
IPv4
TCP
UDP
IPv6
GRE
IPv4
TCP
UDP
IPv6
GRE
VXLAN
VXLAN
Free space in hardware!
Fewer branches!
Lower
cycle count!

## Slide 11: How Do We Get There?
Control plane
Programmable data plane
Abstractions: we can clearly distinguish the inputs to our network programs.
Flexibility: our network devices are programmable and we can change them.
Methodology: approach how to continuously translate inputs to specialization decisions.

## Slide 12: How Can We Deal With Profile Changes?
Introduce a slow, but semantics-preserving fallback path.
😕 Wastes resources and can lead to slow packet processing.
Respecialize unconditionally on every profile change.
😕 Intractable for packet traffic workloads. Thrashing happens on the control-plane side.
Periodically respecialize.
😕 Can lead to profile staleness and needlessly disrupt packet processing.
Is there something better we can do?

## Slide 13: What Does Our Specializer Need To Be?
(1) Control-plane-specializing
Applies program optimizations based on a given control-plane configuration.
(2) Online and Incremental
Handles changes to the control plane without recompiling from scratch.
(3) Semantics-aware
Determines whether a control-plane change requires updating the optimized program.
(4) Fast
Processes semantics-preserving control-plane updates as quickly as possible.

## Slide 14: How Do We Implement This? Use Partial Evaluation!
Specialized P4 Program
Dynamic Input
Static Input
Output
Partial Evaluator
Static input
Data
Program
General program

## Slide 15: Incremental Partial Evaluation
Specialized P4 Program
Packet Input (dynamic)
Control-plane input (static)
Packet output (unchanged)
Partial Evaluator
Control-plane input
Data
Program
P4 program

## Slide 16: An Implementation
Control-plane updates
Control-plane assignments
On semantics change
On every control-plane update
Once
Rate of change:
Specialized P4 program
Data-plane expressions
P4 program
Specialization queries
Dead-code elimination
Constant propagation
Table inlining
For details on this implementation, please see our paper!
16

## Slide 17: Specializing a P4 Program with Queries
Constant substitution: Can I replace this variable with a constant?
Table inlining: Can I replace this map lookup or table call with a statement?
control ingress(Header hdr, bit<9> device_port)
action drop_or_set_port(bool drop, bit<9> port) {
if (drop) {
return;
}
device_port = port;
}
table acl_table {
key = { hdr.eth.src: ternary; }
actions = { drop_or_set_port }
}
apply {
acl_table.apply();
}
}
Match on acl_table?
drop?
Emit packet
device_port:= port
Drop packet
Dependency graph
Dead-code elimination: Can I remove this piece of code?
device_port = 1;
device_port:= 1
device_port = 1;