## Slide 1: XASM: A Foundation to Program the X2 with P4
Fabian Ruffy, Vladimir Gurevich

## Slide 2: Agenda
What is X2 and XISA?
Why XASM?
XASM Concepts
To P4 and Beyond!

## Slide 3: The X2 Switch
12.8Tbps Programmable Switch
  400Gbps/200Gbps/100Gbps ports
  Additional PCIe and Ethernet CPU ports
Ensemble of Data Processing Units (DPUs)
  Programmable Parser
  Programmable Match-Action Processor (MAP)
  Packet buffer, SRAMs, TCAMs
Open Instruction Set Architecture (XISA)
Source: https://xsightlabs.com/wp-content/uploads/2025/03/WN-X-Switch-ISA-WP-Mar2025-1.pdf

## Slide 4: Tofino Native Architecture (TNA)
TNA Switch
Ingress pipeline
Egress pipeline
Packet Replication Engine &
Traffic Manager
Packet Ingress
Packet Egress
packet_in
packet_in
packet_out
packet_out
Ingress Headers Ingress Metadata
Egress Headers Egress Metadata
Straight-through packet flow
Packet data
Programmable Interfaces
Fixed (intrinsic) interfaces
Parser
Parser
Control
Deparser
Control
Deparser

## Slide 5: X2 Programming Model
X2 Data Plane
Follows P4 Model: Fixed-function core with programmable portions
No fixed compute budget, throughput and latency degrades commensurate with complexity.
MAP
ASM
MOV R0.0, R1.3
BRBTSTSET R11.3, 1, do_ipv4
LKPLPM.LF1 R5, R5, NS, NS, R4.4,…
Packet
Parser
ASM
EXTMAP MAPR0, 0, 0, 96
EXTNTXP R3, 96, 16
STHC 14, 3, 1, JUMP_NEXT
Packet
Ingress Port
Egress Port
Data Plane Program
Queue Manager
Programmable packet flow
Entry Points
Packet data
Programmable Interfaces
Fixed (intrinsic) interfaces
Entry Points
Overall Data Plane Algorithm

## Slide 6: An Open ISA and XASM
X-ISA
P4
XASM

## Slide 7: Compiling A Data-Plane Program
X2 Data Plane
Parser
ASM
EXTMAP MAPR0, 0, 0, 96
EXTNTXP R3, 96, 16
STHC 14, 3, 1, JUMP_NEXT
MAP
ASM
BRBTSTSET R11.3, 1, lkp_eth
lkp_eth:
LKP.LF1 R5, R5, NS, NS, 0,…
Parser ASM
EXTMAP MAPR0, 0, 0, 96
EXTNTXP R3, 96, 16
STHC 14, 3, 1, JUMP_NEXT
Control plane objects (Tables, etc.)
Data-plane programming language
Compiler
Assembler
Userland
Device toolchain (Vendor-provided)
Data-plane program
MAP ASM
BRBTSTSET R11.3, 1, lkp_eth
lkp_eth:
LKP.LF1 R5, R5, NS, NS, 0,…
Microcode (X-ISA)

## Slide 8: Down The Switch Stack With An Open ISA
X2 Data Plane
Parser
ASM
EXTMAP MAPR0, 0, 0, 96
EXTNTXP R3, 96, 16
STHC 14, 3, 1, JUMP_NEXT
MAP
ASM
BRBTSTSET R11.3, 1, lkp_eth
lkp_eth:
LKP.LF1 R5, R5, NS, NS, 0,…
Control plane objects (Tables, etc.)
Userland
Need to write this code manually and keep it in sync!
MAP ASM
BRBTSTSET R11.3, 1, lkp_eth
lkp_eth:
LKP.LF1 R5, R5, NS, NS, 0,…
Parser ASM
EXTMAP MAPR0, 0, 0, 96
EXTNTXP R3, 96, 16
STHC 14, 3, 1, JUMP_NEXT
?
?
Microcode (X-ISA)

## Slide 9: Raw X-ISA Program
ingress:
BRBTSTCLR R11.3, 14, not_ipv4_packet
CONCAT.CD R2.2, 0, R1.3, 0, 16
LKPLPM.LF5.R R1.3, R1.3, -1, -1, R2, R2, 0, 4
SYNC.N 32, ipv4_lpm_miss
AQMEG.LF3 R1.0, R1.3
MOVI R1.2, 0
MOVI.CD R0.3, 0
SYNC 8
BRBTSTSET R1.0, 0, aqm_drop
SENDOUT.H R1, R0, 0
not_ipv4_packet:
ipv4_lpm_miss:
aqm_drop:
SYNCALL 255
DROP.H 0
X2 Parser Instructions
X2 MAP Instructions
entry_point_ethernet:
EXTNXTP R0, 96, 16
{// Transition Rules
entry_point_ethernet
0x800: entry_point_ipv4, 0, 0
}
STHC 14, 12, 1, 1
HALT
entry_point_ipv4:
EXTMAP MAPR4, 0, 0, 128
EXTMAP MAPR2, 0, 128, 32
STHC 20, 14, 3, 0
HALT
entry_point_trap:
entry_point_loopback:
entry_point_reparse:
entry_point_fwc:
HALTDROP
Source: https://xsightlabs.com/wp-content/uploads/2025/04/XISA_Simple_IPv4.pdf

## Slide 10: Requirements For Our XDE
1. Make it easy to write data-plane programs and hard to make mistakes.
2. Give the same control/performance as X-ISA.
3. Export the right interfaces to high-level languages.

## Slide 11: XASM
Userland
X2 Data Plane
Parser
ASM
EXTMAP MAPR0, 0, 0, 96
EXTNTXP R3, 96, 16
STHC 14, 3, 1, JUMP_NEXT
MAP
ASM
BRBTSTSET R11.3, 1, lkp_eth
lkp_eth:
LKP.LF1 R5, R5, NS, NS, 0,…
Headers
struct eth {
bit<48> dst;
bit<48> src;
bit<16> type;
}
Tables
table fwd {
key = { bit<48> dst_mac; }
value = { bit<16> qid; }
}
P4
Python/Rust/C
XDP2
NPL
XASM
Data-plane programming language
Compiler
Assembler
XASM Language
Parser
extract_eth:
EXTMAP eth[dst…src]
EXTNTXP eth.type
HALT
MAP
ingress:
BRITSTSET hdr_present(eth), lkp_eth
lkp_eth:
LKP fwd.key, fwd.value, fwd

## Slide 12: XASM Is Inspired By P4
Symbolic programming: All definitions are in the same place and work together.
Control plane interface is an explicit part of the program.
P4
Constants and Types
typedef bit<48> mac_addr_t;
Tables and Externs
action send(port_id_t port) {…}
Parser Code
action drop() {…}
table ipv4_lpm {
key = {
hdr.ipv4.dst : lpm; }
mac_addr_t dst;
mac_addr_t src;
bit<16> etype;
}
actions = { send; drop }
state parse_ethernet {
pkt.extract(hdr.eth);
transition
0x0800 : parse_ipv4;
default: accept;
}
}
Control Code
apply {
if (hdr.ipv4.isValid()) {
ipv4_lpm.apply();
}
}
meta.vrf : exact;
header ethernet_h {
select(hdr.eth.etype) {
XASM
Constants and Types
typedef bit<48> mac_addr_t;
Tables and Externs
Parser Code
table lpm ipv4_lpm {
mac_addr_t dst;
mac_addr_t src;
bit<16> etype;
}
parse_ethernet:
MAP Code
header ethernet_h {
key = {
bit<12> vrf : exact;
ipv4_addr_t ipv4_dst : lpm;
}
value = {
bit<8> sw_control;
bit<16> qid;
bit<8> action;
}
EXT ether_r, ether_p
NXTP ether_r.ethertype
MOVMAP ethernet, ether_r
STHC ethernet_h, \
header_id_t.ETHERNET,\
layer_id.L2, \
X2::NEXT_ON_MISS
HALT
LKPLPM.LF0 lpm_key, tbl_val, ipv4_lpm
SYNC.N [LF0], ipv4_lpm_default
MOV lpm_val, tbl_val
CONCAT lpm_key.vrf, port_meta.vrf
nonip
LDSPI lpm_val, ipv4_lpm_default
BRBTSTCLR hdr_valid[hdr_id.IPV4], \
ingress:
nonip: DROP.H 0

## Slide 13: XASM: Summary
XASM
Macro-assembler with metaprogramming
Functions, macros, and expressions.
Custom errors, imports, conditionals.
Definitions (types, tables, externs).
The goal for XASM definitions is to…
…to make assembly code more readable.
…to generate control plane APIs.
…to combine all programmable X2 elements.
Types
Tables and Extern Definitions
Container Layouts
Parser and MAP Assembly
Control Plane API
Shared Type Definitions
General Meta-programming Facilities
Used by control plane

## Slide 14: From XASM To P4
XASM is still assembly! Assembly is hard.
P4 is our language of choice to support higher-level data-plane programming!
We are building a P4 compiler!
XASM is the foundation for this compiler.
X2 Data Plane
Parser
P4
XASM
MAP

## Slide 15: Header Definitions
typedef bit<48> mac_addr_t;
typedef bit<32> ipv4_addr_t;
enum bit<16> ethertype_t {
TPID = 0x8100,
IPV4 = 0x0800
}
header ethernet_h {
mac_addr_t dst;
mac_addr_t src;
ethertype_t etype;
}
header ipv4_h {
bit<4> ihl;
bit<4> version;
…
ipv4_addr_t src;
ipv4_addr_t dst;
}
enum bit<7> header_id_t { ETHERNET, IPV4, IPV6 };
enum bit<5> layer_id_t { L2, L3 };
XASM
typedef bit<48> mac_addr_t;
typedef bit<32> ipv4_addr_t;
enum bit<16> ethertype_t {
TPID = 0x8100,
IPV4 = 0x0800
}
header ethernet_h {
mac_addr_t dst;
mac_addr_t src;
ethertype_t etype;
}
header ipv4_h {
bit<4> ihl;
bit<4> version;
…
ipv4_addr_t src;
ipv4_addr_t dst;
}
header ipv6_h {
P4

## Slide 16: Extracting an Ethernet Header
parserdef MyParser {
assembly {
parse_ethernet:
assume ethernet_h ether_p in PKT_IN;
TransitionRules {
ethertype_t.IPv4 -> parse_ipv4;
}
EXTMAP ethernet[.dst:.src], ether_p[.dst:.src]
EXTNXTP.CD ether, ether_p.ethertype
MOVMAP ethernet.ethertype, ethertype
STHC ether_h.size_bytes(), \
header_id_t.ETHERNET, \
layer_id.L2, \
X2::NEXT_ON_MISS
HALT
P4
XASM
struct my_headers_t {
ethernet_h ethernet;
}
parser MyParser(pkt_in pkt,
out my_headers_t hdr, …) {
state parse_ethernet {
pkt.extract(hdr.ethernet);
ethertype_t etype = hdr.ethernet.etype;
transition select(etype) {
ethertype_t.IPV4: parse_ipv4;
default: accept;
}
}
state parse_ipv4 {
pkt.extract(hdr.ipv4);
transition accept;
}

## Slide 17: Extracting an Ethernet Header
parserdef MyParser {
assembly {
parse_ethernet:
assume ethernet_h ether_p in PKT_IN;
assume ethernet_h ethernet in R2;
TransitionRules {
ethertype_t.IPv4 -> parse_ipv4;
}
EXTMAP ethernet[.dst:.src], ether_p[.dst:.src]
EXTNXTP.CD ether, ether_p.ethertype
MOVMAP ethernet.ethertype, ethertype
STHC ether_h.size_bytes(), \
header_id_t.ETHERNET, \
layer_id.L2, \
X2::NEXT_ON_MISS
HALT
P4
XASM
struct my_headers_t {
ethernet_h ethernet;
}
parser MyParser(pkt_in pkt,
out my_headers_t hdr, …) {
state parse_ethernet {
pkt.extract(hdr.ethernet);
ethertype_t etype = hdr.ethernet.etype;
transition select(etype) {
ethertype_t.IPV4: parse_ipv4;
default: accept;
}
}
state parse_ipv4 {
pkt.extract(hdr.ipv4);
transition accept;
}

## Slide 18: Extracting an Ethernet Header
parserdef MyParser {
assembly {
parse_ethernet:
assume ethernet_h ether_p in PKT_IN;
assume ethernet_h ethernet in R2;
assume ethertype_t etype in PR0;
TransitionRules {
ethertype_t.IPv4 -> parse_ipv4;
}
EXTMAP ethernet[.dst:.src], ether_p[.dst:.src]
EXTNXTP.CD ether, ether_p.ethertype
MOVMAP ethernet.ethertype, ethertype
STHC ether_h.size_bytes(), \
header_id_t.ETHERNET, \
layer_id.L2, \
X2::NEXT_ON_MISS
HALT
P4
XASM
struct my_headers_t {
ethernet_h ethernet;
}
parser MyParser(pkt_in pkt,
out my_headers_t hdr, …) {
state parse_ethernet {
pkt.extract(hdr.ethernet);
ethertype_t etype = hdr.ethernet.etype;
transition select(etype) {
ethertype_t.IPV4: parse_ipv4;
default: accept;
}
}
state parse_ipv4 {
pkt.extract(hdr.ipv4);
transition accept;
}

## Slide 19: Extracting an Ethernet Header
parserdef MyParser {
assembly {
parse_ethernet:
assume ethernet_h ether_p in PKT_IN;
assume ethernet_h ethernet in R2;
assume ethertype_t etype in PR0;
TransitionRules {
ethertype_t.IPv4 -> parse_ipv4;
}
EXTMAP ethernet[.dst:.src], ether_p[.dst:.src]
EXTNXTP.CD ether, ether_p.ethertype
MOVMAP ethernet.ethertype, ethertype
STHC ether_h.size_bytes(), \
header_id_t.ETHERNET, \
layer_id.L2, \
X2::NEXT_ON_MISS
HALT
P4
XASM
struct my_headers_t {
ethernet_h ethernet;
}
parser MyParser(pkt_in pkt,
out my_headers_t hdr, …) {
state parse_ethernet {
pkt.extract(hdr.ethernet);
ethertype_t etype = hdr.ethernet.etype;
transition select(etype) {
ethertype_t.IPV4: parse_ipv4;
default: accept;
}
}
state parse_ipv4 {
pkt.extract(hdr.ipv4);
transition accept;
}

## Slide 20: Defining a Match Table
table lpm ipv4_lpm {
key = {
bit<12> vrf : exact;
ipv4_addr_t ipv4_dst : lpm;
}
value = {
bit<1> valid;
bit<7> _; /* Padding */
bit<16> qid;
bit<6> _; /* Padding */
bit<2> action; /* Bit encoded */
}
properties = {
size = 65536;
duplicate = X2::DUPLICATE_TO_ALL;
mem_region = "4x4";
cache_enable = true;
}
}
P4
XASM
action send(queue_id_t qid) {
if (X2_is_full(qid)) {
X2_drop();
} else {
X2_simple_send(qid);
}
}
action drop() {
X2_drop();
}
table ipv4_lpm {
key = {
meta.vrf : exact;
hdr.ipv4.dst : lpm;
}
actions = {
send; drop;
}
size = 65536;
}

## Slide 21: Match-Action Table Operation
Header and Metadata Fields
Action Data
Action Code
Action Execution
Lookup Key
Key | Action | Action Data
Default Action | Default Action Data
Hit
Control Plane
Data
Headers and Metadata
(Input)
Headers and Metadata
(Output)
Action
Hit/Miss Selector
Headers and Metadata
1
2
3
4
5
6
7

## Slide 22: Performing Match-Action Operation
mapdef MyMap {
table lpm ipv4_lpm { … }
Assembly {
assume X2::header_valid_t header_valid in R11;
assume ipv4_lpm::key lpm_key in R3.2..R3.3;
assume ipv4_lpm::value table_val in R3.0;
assume ipv4_lpm::value lpm_val in R3.1;
BRBTSTCLR hdr_valid[header_id_t.IPV4], not_ipv4_packet
CONCAT lpm_key.vrf, port_metadata.vrf 1️⃣
LKPLPM.LF0 lpm_key, table_val, ipv4_lpm 2️⃣
LDSPI lpm_val, ipv4_lpm_default_entry 4️⃣
SYNC.N [LF0], ipv4_lpm_miss 5️⃣
MOV lpm_val, table_val /* This is a hit */ 3️⃣
ipv4_lpm_miss:
JTL.NM lpm_val.action, \ 6️⃣
ipv4_lpm_send, ipv4_lpm_drop, ipv4_lpm_done
ipv4_lpm_send:
…
BRI ipv4_lpm_done
ipv4_lpm_drop:
DROP 0
BRI ipv4_lpm_done
ipv4_lpm_done: 7️⃣
…
not_ipv4_packet:
P4
XASM
control MyIngress(inout my_headers_t hdr, …) {
action send() { … }
action drop() { … }
table ipv4_lpm { … }
apply {
. . .
if (hdr.ipv4.isValid()) {
ipv4_lpm.apply();
}
...
}
}

## Slide 23: The Opportunity With the X2: Choice
The open ISA gives you lots of flexibility on the X2 hardware!
Performance scales gracefully.
  Complex data plane code might be slower but always compiles.
  There are many ways to write very efficient code.
How far can we go with P4? We are not sure.
  We are certain about one approach, but there might be others!
  Many P4 architectures can be implemented.
  You can experiment with other languages.
X2 Data Plane
Parser
MAP
XASM
P4

## Slide 24: Build X2 Applications With Us!
The X2 is a new programmable switch on the block.
  It has an open ISA!
We want you to experiment or build data-plane programs on the X2!
  We make this easy with XASM.
  We are working on P4 as the first high-level language to program the X2.
When is this software available? Stay tuned…
  Talk to us! fabianr@xsightlabs.com, vladimirg@xsightlabs.com